## Slide 1
Alec Fredriksson Shannon Lai Simond Liu Wilson Lam
pocketRULER

## Slide 2: Background
Problem:
  Rulers are not compact measuring devices
  Tape measures are limited to measuring straight lines
Wanted a compact device that measures curves and complex geometries for long distances (at least a foot)
Concept was inspired by a tool called a surveyor’s wheel
  Used for measuring distances on the scale of hundreds of feet

## Slide 3: The Product: pocketRULER
Measuring wheel
Feet Indicator
(up to 5 ft)
Inches indicator
(up to 12 in)
Precision indicator (resolution of up to 1/8 in)
PULL TO MEASURE
Alignment arrow

## Slide 4: Design Iterations: Overview
Cycle 1 Cycle 2 Cycle 3
Max distance: 4 feet 1 foot 5 feet
Height: 4.5 inches 3.2 inches 3.9 inches

## Slide 5: Design Changes: Cycle 1 t0 Cycle 2
Shafts are not center
Shifted printing
Print 1
Lessons Learned from Cycle 1
MakerBot has trouble handling prints that take up most of the working surface
Need to increase tolerances
Changes from Cycle 1 to Cycle 2
Removed large gear (measured up to 4 feet)
Can only measure up to 1 foot

## Slide 6: Design Changes: Cycle 2 t0 Cycle 3
Print 2
Lessons Learned from Cycle 2
MakerBot is capable of printing functional gears
Changes from Cycle 2 to Cycle 3
Added Geneva Gear to increase functionality up to 5 feet
Ergonomic contours

## Slide 7: Final Design
Purpose of Geneva gear
  Moves in intervals, unlike a traditional gear, thus smaller size
  Easier for MakerBot to print
  Did not need feet indicator to displayed in between feet
Increased measurement capability from 4 feet to 5 feet from Cycle 1 Design, while decreasing size 15%
Cycle 1 Cycle 2 Cycle 3
http://ilovesmesomeska.deviantart.com/art/Geneva-Drive-63040772
Geneva Gear

## Slide 8: Final Print Results
Printed well
Correct tolerances

## Slide 9: Geneva Gear Analysis
Our Numbers
*inches
http://newgottland.com/2012/01/08/make-geneva-wheels-of-any-size/

## Slide 10: FEA on Wheel
There are 3 main print orientation:
  Up-Right (shown)
  Edge-Up
  Face-Up
Average Human Arm-Hand Weight:
  3.35 kg (7.39lb)  33 N
FEA Tested at:
  10.2 kg (22 lb)  100 N
Maximum Load
  60 lb
Reaction Force from Surface

## Slide 11: Functionality
Can measure up to 5 feet
Accurate to within 1% (only 1/8” deviation when measuring 1 foot)
Meets our objective of being able to accurately measure lines and curves

## Slide 12: Complexity and Difficulty
2 different types of mechanisms
  Spur gear
  Geneva gear
8 separate parts
  2 housings
  2 indicators
  1 intermediate support wall
  2 spur gears
  1 Geneva gear
Tight tolerances needed for gear to mesh properly

## Slide 13: Aesthetics
Housing has ergonomic contours to better fit the user’s hand
Large radius fillets are used to make housing edges more comfortable
Product name is embossed on housing

## Slide 14: Future Improvements
Reduce size of product
  The gears limited the minimum size we could make our product. They needed to be printed large enough such that their teeth were well defined
  By gaining access to a machine with tighter tolerances, it should be possible to reduce the size of our product by 50%
  Possibility of using two Geneva gears
Increase accuracy from 1% to 0.05%
Increase maximum length device can measure
Reset mechanism to go to back to 0 feet

## Slide 15: Questions?
Special thanks to
Professor Li
Injoo Hwang